TIMBER ENGINEERING ENQUIRY ESTIMATE

COMPANY - Active Services   CONTACT- Peter Silcock

TYPE D - SOLID TIMBER RESIN-SPLICE, TRS SIDE SLOT KIT

CATEGORY - +/-3mm ENQ/JOB NO: 1870

SITE - Tavistock Post Office    DATE - 27/09/2004

| D | REPAIR STEPS |
| --- | --- |

| 1 |  |
| --- | --- |

| 2 |  |
| --- | --- |

| 3 |  |
| --- | --- |

| 4 |  |
| --- | --- |

| 5 |  |
| --- | --- |

CONNECTION METHOD - RODS FACTORY FITTED INTO TRS UNIT - EPOXY/STEEL

(NB: 2 Slots illustrated only, for clarity)

Information specified by the Client:

Beam Reference Number

Timber Type

Number to Repair

Width (mm)

Depth (mm)

Overall Repair Length (mm)

1  of  2

SOFT

2

85

225

1600

The output data: (price inc. timber & resins)

Rod Overall Length(mm)

Rod Diameter (mm)

No. of Rods

No. of Slots

Slot Width (mm)

Slot Depth (mm)

Volume of resin, slot filling (L)

Price per beam kit

850

20

3

3

55.5

30

1.95

£181.10

TOTAL PRICE (2 off)

INC. 2.5L PACKS OF TG6

DELIVERY COST

£362.20

2

£61.60

Regardless of the repair system adopted, it can be a legal requirement to provide structural calculations to prove the validity of a proposed structural repair. It is the responsibility of the Contractor to discuss this issue with the Clients professional advisors. We will freely advise a Contractor on where independent structural calculations can be obtained from qualified Structural Engineers.

(D C MOORE 1997

David Moore - Timber Repair Systems

Tel:	+44 (0)1626 331351

Fax:	+44 (0)1626 331143

e-mail:	dcmoore@timber.org.uk

See our INTERNET SITE at:

http://www.timber.org.uk/

or our Leaflet  (LDRT 1297/2)

NO

NO